## Slide 1: SMC-3010 to MP2600iec Conversion
PN.MP2600iec.01

## Slide 2: SMC3010 and Legend Amplifier
Facts
  Introduced 10 years ago in March 2001
  Average sales of about 1000 controllers per year
  Based on Galil 1400 series controller
    Programming and command structure based on 80’s and 90’s technology
  Simple yet powerful capability at a good price
  MP2600iec offers basically the same features, but the two controllers are completely different animals
    MP2600iec offers many modern conveniences missing in the SMC product
  Translating a program from SMC to IEC is not straightforward
    Recommend understanding the application requirements and start over
    Don’t attempt a line by line translation.
    We can recommend a conversion approach on an application by application basis

## Slide 3: Hardware Comparison
SMC3010
MP2600iec / Sigma-5
  1.5 axis controller
  1.5 axis controller plus virtual master capability
  15 input 11 outputs
  12 inputs, 4 outputs
  Sinking I/O @ 200 mA
  Sink / Source I/O @ 50mA
  High speed output @ 13 uSec
  +24 VDC opto isolated
  High speed output @ 600 nSec
  +5 VDC no opto isolation
  Power obtained from SGDV
  Power obtained from SGDG

## Slide 4: Programming Comparison
SMC3010
  Multi tasking environment, 4 tasks
  Multi tasking environment, 16 tasks
  Programming style: (standard)
  IEC 61131
    Ladder Diagram
    Structured Text
    Sequential Function Chart
  PLCopen for Motion Control
  Programming style (proprietary):
  Structured text language
  Two letter mnemonic command interface
  Behavior:
  Tasks are run as scripts from one command to the next
  No scan time is implied
  More commands mean more time required to execute
  Only the active command in each task is active at any one time
  Behavior:
  Programs of the various styles described above are inserted into cyclic tasks and all code is executed within the cycle time setting, or a watchdog alarm occurs.
MP2600iec

## Slide 5: Motion Feature Comparison
SMC3010
MP2600iec
  Distributed Motion Control
  a.k.a
  Virtual Multi Axis Controller
  IEC 61131 specifies multi resource (controller) support, but MotionWorks IEC does not offer this feature yet. Use MP2300Siec.
  Gearing:
  Change ratio on the fly
  Synchronize slave to master over specific distance
    MC_GearInPos
  Gearing:
  Change ratio on the fly
  Synchronize slave to master over a specific distance
    GD command
  Camming:
  Fixed number of data points
  Fixed master interval
  One table at a time
  Cannot change master slave shift on the fly.
  Camming:
  Virtually unlimited data points
  Variable master interval
  Virtually unlimited number of tables
  Change offset, shift and scaling, even tables on the fly.

## Slide 6: Motion Feature Comparison
Distributed Motion – Virtual Multi Axis Controller
  MP2300Siec
    Use Mechatrolink instead of SMC Ethernet
    MP2300iec BENEFIT:
      Alarm data from all servopacks
      Parameter data to/from all servopacks
    SMC3010 DRAWBACK:
      Distributed Control only provided data to/from other controllers.
  Multiple MP2600iec controllers
    Future Multi Resource support for MotionWorks IEC Pro will make it easier to program multiple MP2600iec controllers in a system.
      One project for all

## Slide 7: Communication Differences
SMC3010
MP2600iec
  Hardware:
  Serial @ 19200
  Ethernet @ 10BaseT
  Hardware:
  No serial support
  Ethernet @ 100BaseT
  Protocols:
  Serial:
    n/a
  Ethernet:
    Modbus
    Ethernet/IP
    OPC (windows platform)
    HTTP (webserver)
  Protocols:
  Serial:
    Simple ASCII 8, bit
  Ethernet:
    ASCII / Telnet
    Modbus TCP
  Behavior:
  MG Command can send event based or cyclic messages, either ASCII or Modbus
  Behavior:
  Modbus and Ethernet/IP are synchronized with a cyclic task.

## Slide 8: Special Feature Comparison
SMC3010
MP2600iec
  Absolute Encoder Support:
  None
  Absolute Encoder Support:
  Yes. Home offset automatically stored in battery backed RAM
  Amplifier parameter support:
  Yes, via PLCopen function block
  Amplifier parameter support:
  Yes, limited to 5 Pns that Legend supported. (PN command)
  Analog Feedback Mode:
  No built in mode, but tools exist to implement:
  PID_Control function block
  Y_DirectControl function block
  Analog Feedback Mode:
  AF command selects the analog input as the position feedback for the PID loop.
  Dual Encoder Feedback:
  DV command
  Dual Encoder Feedback:
  No built in mode
  Use PID_Control function block and build your own motion profiler.

## Slide 9: Feature enhancements available
Sigma-5 Amplifier Technology
  Tuneless mode
  Vibration suppression
  Absolute encoder
  Built in motor brake control functionality
  Direct drive motor support
  Increased capacity range of SigmaV (to 15kW)
  Safety stop input (Hardware Base Block)
  RoHS components

## Slide 10: Feature enhancements
Controller Technology
  Higher level programming languages (IEC 61131)
    User defined structures
    Object orientated programming
  Scan based execution
  64 bit floating point
  More built in motion features via PLCopen function blocks
  Increased camming flexibility
  Alarm history
  Project Archive